# Text boxes

##### Ledger Panels: Gold Rush

M S International, Inc.

# Premium Surfaces Since 1975

## Substrates

## Exterior/Interior

- Fully cured concrete (at least 28 days cured)

- Masonry brick

- Regular brick

- Cement mortars

- Cementitious backer units

## Interior only

- Gypsum plaster (max 10’ high)

- Gypsum wallboard (max 10’ high)

- Exterior grade plywood (max 10’ high)

- Cementitious backer units

#### Sizes

- Flat panels: 6 x 24”

- Corner:       6 x 6 x 6”

#### Packaging

- Panels: 6 pcs/box; 180 pcs/crate

- Corner: 12 pcs/box; 240 pcs/crate

Thickness: 	0.5-0.75”

Color: 		Dark gray, rusty orange

Type: 		Slate

Application: 	Walls, barbeque areas, etc.

###### Technical Information

- Average Compressive Strength:

#### Dry/4931 Psi

#### Adhesive

- Exterior application: a flexible latex based mortar system suitable for the stone is recommended.

- Interior application: a thin set mortar suitable for the stone is recommended.

- For light colored stones, a white mortar is recommended.