# Text boxes

##### Ledger Panel: Golden Honey

M S International, Inc.

Premium Surfaces Since 1975

## Substrates

## Exterior/Interior

- Fully cured concrete (at least 28 days cured)

- Masonry brick

- Regular brick

- Cement mortars

- Cementitious backer units

## Interior only

- Gypsum plaster (max 10’ high)

- Gypsum wallboard (max 10’ high)

- Exterior grade plywood (max 10’ high)

- Cementitious backer units

#### Packaging

Panels: 	6 pcs/box; 210 pcs/crate

Corner: 	6 pcs/box; 240 pcs/crate

Color: 				Green/White/Gold

Application: 	Walls, barbeque areas, water features, etc.

###### Technical Information

- Flat Panel:  6”x 24”

- Corner:  6”x 12”x 6”

- Thickness:  .75 to 1.5”

- Weight:  6.86 lbs.

- Material:  Quartzite

- Finish:  Splitface

- Average Compressive Strength:

Dry/7800 Psi

#### Adhesive

- Exterior application: a flexible latex based mortar system suitable for the stone is recommended.

- Interior application: a thin set mortar suitable for the stone is recommended.

- For light colored stones, a white mortar is recommended.